# Encounter manual

# Guangyi CAO

Cadence Encounter is a software for placement and routing of synthesized vhdl (verilog) code.

To start with Encounter in linux, type Encounter in your home directory, then Encounter graphic user interface displays.

Create a folder, for example, neededfile, and put all needed files in it.

Necessary files should include:

1. A synthesized verilog file, like fpu_sin.v, or your own design.

2. Timing libraries, we use typical_conditional_ecsm.lib

3. lef file, free2008_10_sp1.lef

4 a clock tree file, clock.ctstch.

## Import design

## In encounter GUI, click design->import design, the following frame comes out, input all needed information like this. Please notice for top cell, you can choose Auto Assign.

Figure 1

Figure 2

Then click advanced->power, change power and ground nets as VDD, VSS.

Click Ok, load design will start. After it finished, see what happened in command window.

Figure 3 After loading design

Floorplan

Click floorplan-> specify floorplan, notice the core utilization should not be over 0.75, or else the chip will be too crowded. Core to left, right, top and bottom as 5. click Ok.

Figure 4

Add power ring

Power->power planning-> add rings, click ok. Click the physical view button at the right upper side and you will see

Figure 5

Add power stripe

Power->power planning-> add stripes, the following frame will come out. Change the set-to-set distance to be 20 as the width of current design is only 64 and the default is 100.

Figure 6

Figure 7 after add rings and stripes

placement

click place-> standard cell->ok, it should look like this. If you cannot see it, click physical view button again.

Figure 8 after placement

Clock tree synthesis

Click clock->design clock, change clock tree specification file to be our file, clock.ctstch, click OK. Clock tree synthesis will be executed.

Figure 9, After clock tree synthesis

Nanoroute

Click route->nanoroute->route, click Ok.

Save design

Click design->save->def, in the frame coming out, choose your desired directory in store the file, rename the file if you want.

Report power

Click power->report power, choose proper name and directory for the report file and click Ok

Congratulations! You have done your first encounter exploration!