## Slide 2: Color Schlieren Imaging of Internal Shock Structure in Super Sonic Planar Rocket Nozzle
Conclusions
Simple, inexpensive, safe tests and the results are spectacular.
  From the parabolic nozzle, we see the shock formation inside throughout the nozzle
  We had a clear Restricted Shock Separation (RSS) during the low pressure test on the parabolic nozzle.
  The conical nozzle showed clear Free Shock Separation (FSS)
Introduction
Numerous failures have resulted due to a lack of understanding concerning side-load issues.
Visualization techniques can help in the analysis of side-load failure mode. Color Schlieren imaging is a useful techniques for exploring the side-loading phenomena.
Goals
Use a color Schlieren imaging system to visualize the shock structure inside a rocket nozzle. Test at high nozzle pressure ratios (NPR > 100). In particular, look for Shock Separation. Use this to look for the source of rocket side loads.
Separation (FSS) and Restricted Shock Separation (RSS)
Peter Tkacik 1, Russell Keanini 2, Nilabh Srivastava3, Sam Hellman4, University of North Carolina at Charlotte, Michael P. Tkacik5, Clemson University, Den Baseda6, North Carolina State University
1ptkacik@uncc.edu, 2rkeanini1@uncc.edu, 3nsrivast@uncc.edu, 4shellma3@uncc.edu, 5mtkacik@clemson.edu, 6dbaseda@ncsu.edu
Light rays
Rocket Nozzle
Mirror stand
Mirror stand
Knife edge
Camera
High pressure lines
High pressure tank and ball valve
Light source
Planar Rocket nozzle
Mirror #1
Mirror #2
Color light source
Circular knife edge and camera
High pressure Argon tank
Above and below are the images sequenced from zero pressure up to about 150 MPa (2200 psi) and then slowly back down to ambient showing a collection of internal shocks and Mach waves
Figure 1. The Apollo Astronauts were shaken so badly by nozzle side load problems that they reportedly couldn’t see the emergency eject button (NASA image).
The high pressure ratio nozzle:
Modified for a variety of nozzle geometries
Steel and high strength tempered glass panes
High pressure tank
A high pressure tank and a ball valve for fast pressure response was charged with Argon gas to 150 MPa can be recharged quickly for repeat experiments.
Test Run
Capture test firings with digital high definition CCD camera Blu-Ray© (*.M2TS) format at 30 fps
Experiment run times 10 seconds with maximum pressure for only 0.10 seconds
Results of experimental color Schlieren imaging of internal rocket nozzle flow:
Nominal maximum mach number (NMMN) 4.4
Flow field image compared well against CFD results.
Nominal maximum mach number (NMMN) 2 revealing Restricted Shock Separation (RSS)
Figure 4. Test fixtures
Figure 3. Test schematic
Figure 2. Nozzle